## Slide 1
Developing an Automated Spectrophotometer with RGB LED and LDR Sensor Using Arduino Microcontroller
Ethan Cha, Hayden Lee, Bergen County Academies, United States
Q1: Research Questions:
The research focuses on developing a spectrophotometer using RGB led, LDR sensors, 3D printed sampling cartridge, and Arduino Mega. This was conducted to show viability of RGB Spectrophotometer using inexpensive technology in conjunction to systematic programming to reproduce commercial spectrophotometers
Q2: Methodology/Project Design:
Using the Arduino Mega as the central board, different parts were used to allow user input (Keypad), shine RGB light (led), quantify light intensity (LDR sensor), rotate cuvettes (stepping motor, Sample insert cartridge), and display the results (LCD
Q3: Data Analysis & Results:
Q4: Interpretation & Conclusions:
Our RGB spectrophotometer was assembled with the RGB led, LDR sensors, 3D printed sampling cartridge, and Arduino mega with automation software to select wavelength, calculate calibration parameters, and report the concentration of the studied material. The RGB spectrophotometry could measure, as seen in the figures above, from food dyes, gold colloids, methylene blue, Eosin, turbid water, and multivitamins. In most cases, the regression coefficient was higher than 0.995. At some point, the regression coefficient was even more significant than that from commercial spectrophotometry. The study confirmed the feasibility of developing an RGB spectrophotometer with high accuracy and precision.
Display). A custom program was created to read the first 6 cuvettes, calculate the best light according to the R2 formula, and then quantify the density of the solution for the next 10 cuvettes with the same type of solution. Finally, the LCD displays the results of the density.
This table shows the result of a T-Test; the accuracy deviates by around 2%, and the precision by 3-5%. These numbers could surely be reduced.
Our results are structured such that the bottom graph is an expanded version of the leftmost points of the top graph. This is for reader clarity.
The results are incredibly promising, all except two showing higher than .99 as its regression coefficient.